TIPS TO REDUCE RISK

OF TERMITE ATTACKS

Source:  Mike Potter

Homeowners can reduce the risk of termite attacks that annually cause billions of dollars in damage in the United States.

Since termites are attracted to moisture, it is important to reduce consistent wetness in soil around the foundation as well as humidity in crawl spaces.

Use properly functioning gutters, downspouts and splash blocks to divert water away from the foundation.  Also, repair leaking faucets, water pipes and air-conditioning units.  Be sure the soil grade next to the foundation directs surface water away from the structure, and adjust lawn irrigation systems and sprinklers to minimize water puddles near the foundation.

Providing adequate ventilation reduces the humidity in crawl spaces.  Prune shrubbery and other vegetation growing over vents to improve cross-ventilation.  To reduce moisture, install four- to six-milliliter polyethylene over about 75 percent of the soil surface.

Many termite infestations result from direct structural wood-soil contact that gives termites access to food, moisture, shelter and a hidden entry into the home. To avoid this situation, be sure there are at least six inches between ground level and wooden elements such as siding, porch steps, latticework, door and window frames and posts.

Remember that termites also are attracted to, and may infest, firewood, lumber and other wood debris stored against the foundation or in crawl spaces.  These wooden elements enable termites to bypass an existing termiticide soil barrier.

Termites are especially attracted to moisture retained below cellulose-containing materials like mulch and wood chips.  Use mulch sparingly, especially if other conditions are conducive to termite problems. Two to three inches is usually plenty of mulch. Do not let it come into contact with wood siding and door or window frames.

For more information, contact the (County Name) Cooperative Extension Service.

Educational programs of the Kentucky Cooperative Extension Service serve all people regardless of race, color, age, sex, religion, disability or national origin.

-30-